## Slide 1
  Message decoded to be transmitted for moving vehicle at a speed of 1m/s.
  ID: 0x130 (A2V_DriveCtrl)
 | Bit Order | MSB | → → → → → → → → |  |  |  |  |  | LSB | HexaDecimal
 | bit order |  |  |  |  |  |  |  |  | 
Byte Order |  | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | 
MSB | Byte 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0x11
↓ | Byte 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0x64
↓ | Byte 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0x00
↓ | Byte 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0x00
↓ | Byte 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0x00
↓ | Byte 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0x00
↓ | Byte 6 | 0 | 0 | 0 | 0 | 0→1 | 0→1 | 0→1 | 0→1 | 0x00 → 0x0F
LSB | Byte 7 | Byte 0 XOR Byte1 XOR Byte2 XOR Byte3 XOR Byte4 XOR Byte5 XOR Byte6 |  |  |  |  |  |  |  | ---------------
  (Byte 0) 0x11: Signify Vehicle Drive Control Enable is Enabled, Used in Speed Control Mode in Drive Gear.
  (Byte 1) 0x64: It is only valid in Speed Control Mode. So for 1m/s speed, we have to give a decimal value of (1/0.01 = 100) where 0.01 is the given factor and 100 = 0x64.
  (Byte 2) 0x00: As speed control mode is used, we will keep the throttle mode to 0.
  (Byte 3) 0x00: No description is given for this.
  (Byte 4) 0x00: No description is given for this.
  (Byte 5) 0x00: No description is given for this.
  (Byte 6) 0x00 → 0x0F: Keep Adding 1 to the last 4 bits until it becomes F and then repeat from 0.
  (Byte 7): We must do XOR of all the first 7 bytes to make it a checksum value.

## Slide 2
  Message decoded to be transmitted to stop vehicle motion by applying break.
  ID: 0x131 (A2V_BrakeCtrl)
 | Bit Order | MSB | → → → → → → → → → |  |  |  |  |  | LSB | HexaDecimal
 | bit order |  |  |  |  |  |  |  |  | 
Byte Order |  | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | 
MSB | Byte 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0x03
↓ | Byte 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0xC8
↓ | Byte 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0x00
↓ | Byte 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0x01
↓ | Byte 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0x00
↓ | Byte 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0x00
↓ | Byte 6 | 0 | 0 | 0 | 0 | 0→1 | 0→1 | 0→1 | 0→1 | 0x00 → 0x0F
LSB | Byte 7 | Byte 0 XOR Byte1 XOR Byte2 XOR Byte3 XOR Byte4 XOR Byte5 XOR Byte6 |  |  |  |  |  |  |  | ---------------
  (Byte 0) 0x03: Signify Vehicle Break Enable and brake light will be on when break applied.
  (Byte 1) 0xC8: When a vehicle is moving, we will apply 20% of break which is (20/0.1 = 200 in decimal) where 0.1 is the given factor and 0b200 = 0xC8 in hexadecimal.
  (Byte 2) 0x00: No description is given for this.
  (Byte 3) 0x01: This is Parking Control which will be 1 for applying brake.
  (Byte 4) 0x00: No description is given for this.
  (Byte 5) 0x00: No description is given for this.
  (Byte 6) 0x00 → 0x0F: Keep Adding 1 to the last 4 bits until it becomes F and then repeat from 0.
  (Byte 7): We must do XOR of all the first 7 bytes to make it a checksum value.

## Slide 3
  Message decoded to be transmitted to move steering of vehicle.
  ID: 0x132 (A2V_SteerCtrl)
 | Bit Order | MSB | → → → → → → → → → |  |  |  |  |  | LSB | HexaDecimal
 | bit order |  |  |  |  |  |  |  |  | 
Byte Order |  | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | 
MSB | Byte 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0x11
↓ | Byte 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0x64
↓ | Byte 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0x00
↓ | Byte 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0x00
↓ | Byte 4 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0x0A
↓ | Byte 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0x00
↓ | Byte 6 | 0 | 0 | 0 | 0 | 0→1 | 0→1 | 0→1 | 0→1 | 0x00 → 0x0F
LSB | Byte 7 | Byte 0 XOR Byte1 XOR Byte2 XOR Byte3 XOR Byte4 XOR Byte5 XOR Byte6 |  |  |  |  |  |  |  | ---------------
  (Byte 0) 0x11: Signify enables steering control along with the type of vehicle control. 0x11 is for control of front and rear steering at the same angle.
  (Byte 1) 0x64: It signifies the steering angle for the selected mode in byte 1 for the front wheels.
  (Byte 2) 0x00: 0x00 describe +ve (means right direction) movement of wheels. 0xFF will be for left-direction movement. This is for front wheels.
  (Byte 3) 0x00: It signifies the steering angle for the selected mode in byte 1 for the rear wheels.
  (Byte 4) 0x00: 0x00 describe +ve (means right direction) movement of wheels. 0xFF will be for left-direction movement. This is for the rear wheels.
  (Byte 5) 0x0A: This describes the angular velocity by which wheels should move.
  (Byte 6) 0x00 → 0x0F: Keep Adding 1 to the last 4 bits until it becomes F and then repeat from 0.
  (Byte 7): We must do XOR of all the first 7 bytes to make it a checksum value.

## Slide 4: Transmitted Messages for Pixkit Control using SavvyCAN
For vehicle speed
ID: 0x130 Transmitted Message:
For Brake Control
ID: 0x131 Transmitted Message:
For Steering Control
ID: 0x132 Transmitted Message:
Byte 0 | Byte 1 | Byte 2 | Byte3 | Byte 4 | Byte 5 | Byte 6 | Byte 7
0x11 | 0x64 | 0x00 | 0x00 | 0x00 | 0x00 | 0x00 → 0x0F | XOR of Byte 0 to Byte 6
Byte 0 | Byte 1 | Byte 2 | Byte3 | Byte 4 | Byte 5 | Byte 6 | Byte 7
0x03 | 0xC8 | 0x00 | 0x01 (To Apply Handbrake) 0x02 (To remove Handbrake) | 0x00 | 0x00 | 0x00 → 0x0F | XOR of Byte 0 to Byte 6
Byte 0 | Byte 1 | Byte 2 | Byte3 | Byte 4 | Byte 5 | Byte 6 | Byte 7
0x11 | 0x64 | 0x00 | 0x00 | 0x00 | 0x0A | 0x00 → 0x0F | XOR of Byte 0 to Byte 6